## Slide 1: 11 and 13 October Photonics-PPT#2 LED LASER LIGHTING
One More slide on “Bandgap” Engineering From PPT#1

## Slide 2: Photon Emission in Semiconductor
EF
EC
EV
Conduction band
Valence band
Photon
Eg
When an electron meets a hole, it falls into a lower energy level, and releases energy in the form of a photon.
The wavelength of the light depends on the band gap of the semiconductor material
Semiconductor materials: Si, Ge, GaAs, InGaAs, AlGaAs, InP, SiGe, etc

## Slide 3: Light-Emitting Diodes (LEDs)
Light-emitting diode (LED) is a semiconductor diode that emits incoherent light over relatively wide spectral range when electrically biased in the forward direction of the p-n junction.

## Slide 10
CYMK (Cyan, Magenta, Yellow, Black) Printing
Also Watercolor, Oil, Acrylic Painting
Displays, Imaging

## Slide 21: Laser Diodes
Lasers (Light Amplification by Stimulated Emission)
Photon emission processes:
Absorption
Photodetectors
Spontaneous emission
LEDs
Stimulated emission
Lasers

## Slide 22: Laser Cavity Design
GaAs N+
GaAs P+
Current
Total reflector
Partial reflector
Electrodes
Laser cavity design:
Laser medium is similar to LEDs,
Extra components a in laser cavity are the mirrors at two facing planes (facets) for lasing mode selection.
The laser light is monochromatic and coherent due to the mode selection in the cavity design

## Slide 25: Application of QWs — Diode Laser
25
25
Disadvantages:
Emission wavelength depends on material
Very difficult to generate more than one color per laser
Difficult to generate long wavelength, i.e., colors in the mid- to far- infrared region
n-AlGaAs
GaAs
p-AlGaAs
Electrode
+V
Conduction band
Valence band
Band gap
Electrode
Light
Light

## Slide 26: Semiconductor Quantum Wells (QWs)
26
26
A narrow gap semiconductor is sandwiched between layers of a wide band gap
semiconductor
Quantum confinement takes place when the well thickness is comparable to De
Broglie wavelength of the particle
Electron movement is confined in the quantum well growth direction
Examples: GaAs/AlAs, InGaAs/AlInAs.

## Slide 27: Photo Diodes (PDs)
A photodiode is a semiconductor diode that functions as a photodetector. It is a p-n junction or p-i-n structure. When a photon of sufficient energy strikes the diode, it excites an electron thereby creating a mobile electron and a positively charged electron hole
PD symbol: