## Slide 1: II-VI Semiconductor Materials, Devices, and Applications Lorelei Lewandowski 4/20/2015
There are 7 II-VI semiconductor materials. Because of their direct, wide band gap energy, they are becoming increasingly useful in optical applications. While some of them have been around for many years, research is still needed to determine the full potential of others. The “latest and greatest” technology in the near future will most likely owe much of its success to these materials.

## Slide 2: Outline/Intro
List of II-VI Semiconductor Materials
General Common Properties
Common Usage of Each
Overview/Conclusion
References
Concept Check

## Slide 3: The 7 Materials
Zinc Oxide
Zinc Sulfide
Zinc Selenide
Zinc Telluride
Cadmium Sulfide
Cadmium Selenide
Cadmium Telluride

## Slide 4: Process
The growth methods vary by material, but there are various types used with each one. The growth method used depends on the application that is needed.

## Slide 5: Direct band gaps
No change in momentum takes place, so light can be emitted in the form of a photon, which is necessary for optical devices.

## Slide 6: Wide band gap
These 7 materials have band gaps ranging from 1.5eV to 3.54eV.
Perspective: Si has a band gap of 1.1eV and GaAs 1.4eV.
A wider band gap is one property that these materials have in common. Because of this, they have various common applications such as:
  LEDs & LDs
  Signal Processing

## Slide 7: advantages
Higher Iconicity & Stronger Bonds = Higher Melting Temp
Less Energy Lost = More Efficient & Potential For Lower Cost
Higher Breakdown Voltage = High Power & Freq Applications
Higher Doping Concentration = Thinner Device Layers
Higher Electron Mobility = Faster Operation

## Slide 8: Zinc Oxide (ZnO)
3.3eV Band Gap Energy
Doping is n-type
Abundant & Non-Toxic
Strong Piezoelectric (converting mechanical energy into electrical energy) Effect
Used in Nanogenerators

## Slide 9: nanogenerators
Currently Being Researched
Many applications
  Wind/Water
  Human Body – Biomedical
KAIST in Korea in 2014: 130V
Issues
  Power Supply
  Low Output Current
  Unknowns That May Affect Surface Charge Density

## Slide 10: Zinc Sulfide (ZnS)
3.54eV Band Gap Energy
Doping is p-type or n-type
Used in Cathode Ray Tube
Detects Alpha Radiation (via Scintillation)
Scintillation was done in the early 1900s before the nucleus was discovered.

## Slide 11: “Glow In The Dark”
Phosphorescence
Silver Added For Blue Glow
Manganese For Orange/Red Glow
Copper Usually Added
  Common Green Glow
  Glow Lasts Longer

## Slide 12: Zinc Selenide (ZnSe)
2.82 eV Band Gap Energy
Doping is n-type
Used As Lenses In High Power CO2 Lasers

## Slide 13: Zinc Telluride (ZnTe)
2.26 eV Band Gap Energy
Doping is p-type
Background Layer in Solar Cells
Tellerium is found in the Earth’s crust, but is very rare.
  (About 1-5 Parts Per Billion)
THZ detection and generation

## Slide 14: Thz signals
Used For:
  Medical Imaging
  Security
  Spectroscopy

## Slide 15: Cadmium Sulfide (CdS)
2.42 eV Band Gap Energy
Doping is n-type
Mainly Used As Pigment
Used in Photoresistors

## Slide 16: Cadmium Selenide (CdSe)
1.74 eV Band Gap Energy
Doping is n-type
Can Be Used as Layer in CdTe Solar Cells
Most Research Focused On Nanoparticles– Quantum Dots

## Slide 17: Quantum dots
Quantum dots, discovered in 1981, are nanoscale “dots” of semiconducting material.
They glow a specific color when hit with light.
Applications include LCD LED Tvs, photonics, medical diagnostics, biomedical imaging, etc.

## Slide 18: Cadmium Telluride (CdTe)
1.5 eV Band Gap Energy
Doping is p-type
Issues with Cadmium’s Toxicity
2nd most utilized solar cell in the world
CdTe solar panels are the only ones that have surpassed the cost efficiency of polycrystalline Silicon solar panels.
Just last month First Solar set the world record for thin film CdTe solar panel efficiency at 18.7%!
They believe they can achieve up to 23%.

## Slide 19: Solar power
CdTe is very close to GaAs in efficiency.
GaAs behavior is used to predict future CdTe efficiency trends.

## Slide 20: SUMMARY & CONCLUSION
  II-VI semiconductor materials are becoming increasingly important in the semiconductor industry. Nanogenerators have the potential to change the future of electronics while quantum dots and solar panels are integrating themselves into modern electronics. While it’s impossible to determine just how large of an effect these materials will have and how long-lived they will be, high power electronics and the medical industry are already benefiting from them.

## Slide 21: REFERENCES
Academic Sources (Articles, Textbooks, IEEE Spectrum)
  http://psec.uchicago.edu/library/microchannel_plates/zinc_oxide.pdf
  https://books.google.com/books?id=qCebxPjdSBUC&pg=PA110&lpg=PA110&dq=radioactive+decay+zns&source=bl&ots=H2NiCPCG8P&sig=4JyD-vteNbBwENaQYiovVmpJl0s&hl=en&sa=X&ei=3rQwVfyPJ4yZsAWdkYC4Dw&ved=0CCYQ6AEwAg#v=onepage&q&f=false
  http://scholar.lib.vt.edu/theses/available/etd-04262005-181042/unrestricted/Ch1Applications.pdf
  http://link.springer.com/article/10.1007%2Fs00216-007-1661-9#page-1
  http://spectrum.ieee.org/tech-talk/semiconductors/nanotechnology/energy-harvesting-nanogenerators-give-130-volts-at-the-touch-of-a-finger
Websites
  http://www.azom.com/article.aspx?ArticleID=8415#5
  http://www.firstsolar.com
  http://mpsd-cmd.cfel.de/research-met-thz-optrect.html
  http://www.iiviinfrared.com/Optical-Materials/znse.html

## Slide 22: KEY CONCEPTS
Wide/Direct Band Gap – Importance in Photonics
What are nanogenerators?
What causes things to “glow in the dark”?
Quantum Dots Applications
Solar Panel Innovation by CdTe