## Slide 1: OLEDs – THEORY AND FABRICATION
ABSTRACT: Organic Light Emitting Diodes are quickly becoming the cutting edge in display technology. This presentation will give a brief history of OLEDs, the theory behind organic semiconductors, the physics behind OLEDs, and then go into different fabrication techniques. The apparent advantages and disadvantages of OLEDs will also be examined.
Nick Robillard 5/1/15

## Slide 2: OUTLINE
History
Organic Semiconductors
Physics of OLEDs
Fabrication
Advantages/Disadvantages

## Slide 3: HISTORY OF OLEDs
  1862 – Henry Letheby
    1st partly conductive polymer: polyaniline
  1950s – Andre Bernanose
    1st observation of organic electroluminesce
  1960 – Martin Pope
  Developed ohmic dark-injecting electrode contacts for organic crystals
    basis for charge injection in all modern OLED devices
  1977 – Hideki Shirakawa
    high conductivity in iodine-doped polyacetylene
    Awarded Nobel Prize in Chemistry
  1987 – Ching Tang & Steven Van Slyke
    first organic diode device for Eastman Kodak
http://www.npg.org.uk/collections/search/portraitLarge/mw124586/Henry-Letheby?LinkID=mp87183&search=sas&sText=Letheby&OConly=true&role=sit&rNo=0

## Slide 4: History of OLEDs(cont)
  1990 – JH Burroughs
    High efficiency green light emitting polymers
    Sheets 100 nm thick
1998 – Kodak & Sanyo
  Full-Color AMOLED
2007 – Sony
  First OLED TV in Japan
2010 – Samsung
  7 inch Super-AMOLED display
2012 – LG
  55 in TV display

## Slide 5: Organic Semiconductors
Carbon polymers
Plastic
Insulator?
Doping
  Heeger, MacDiarmid, and Shirakawa
  Oxidize a thin film of polyacetylene with iodine vapor
  Increase conductivity a billion times
Much like doping of conventional semiconductors

## Slide 6: ORGANIC SEMICONDUCTORS(cont.)
Conductive Polymer
  Conjugate double bonds
  Doping
Oxidation (P-doping)
  Halogen gas
  Ex.) [CH]n + 3x/2 I2 --> [CH]nx+ + x I3-
Reduction(n-doping)
  Alkali metal
  Ex.) [CH]n + x Na --> [CH]nx- + x Na+
Polyacetylene
http://www.nobelprize.org/nobel_prizes/chemistry/laureates/2000/popular.html

## Slide 7
π and σ Bonds

## Slide 8: Organic Semiconductors(cont.)
Most organic materials are intrinsically p-type
Higher hole mobility than electron mobility
  Opposite of non-organic semiconductors
Trap states
  Electrons more susceptible to trapping
  Impurities frequently have empty orbitals (that trap electrons) below -3eV
  Filled orbitals (which trap holes) above -5eV are not as common
http://www.nature.com/nmat/journal/v11/n10/full/nmat3427.html?WT.ec_id=NMAT-201210

## Slide 9: Physics of OLEDs
Cathode
Emissive layer
  “N-type” polymer
  Ex.) polyfluorene
Conducting layer
  “P-type” polymer
  Ex.) polyaniline
Anode
http://electronics.howstuffworks.com/oled1.htm

## Slide 10: Physics of OLEDs(cont.)
Electrophosphorescence
  Voltage applied across device
  Electron-hole recombination
Energy released in the form of light
  ∆ E = E(LUMO) – E (HOMO) = h ν = h c / λ
Different emissive polymers emit different wavelengths of light
  Displays will use several types of organic lights to make the different colors
http://ieeexplore.ieee.org/ielx5/6329165/6338451/6338465/html/img/6338465-fig-2-small.gif
http://www.nobelprize.org/nobel_prizes/chemistry/laureates/2000/advanced-chemistryprize2000.pdf

## Slide 11: Physics of OLEDs(cont.)
Operating voltage: 2-10V
Very dynamic
  Can emit all steps between 0% and 100% light, depending on the current
V-I Characteristic
  Hysteresis for different sweep directions
  Transient behavior likely from deep traps
http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=1503740

## Slide 12: Fabrication of OLEDs
General layout
Three Types:
  Vacuum Deposition/Vacuum Thermal Evaporation(VTE)
  Organic Vapor Phase Deposition
  Inkjet Printing
http://ieeexplore.ieee.org/xpls/icp.jsp?arnumber=6338465

## Slide 13: Vacuum Thermal Evaporation
Very low pressure (10-6 or 10-5 Torr)
Organic molecules heated until evaporation
Condense on a cooled substrate
Thickness of each layer can be precisely controlled
Disadvantages:
  Evaporant condensed on cold walls can flake off, contaminating the system and substrate
  Controlling uniformity and doping concentration over large areas are very difficult
  Very expensive and inefficient

## Slide 14: Organic Vapor Phase Deposition
Process:
  Organic compound is thermally evaporated
  Fed into a diluting, non-reactive gas stream(such as nitrogen)
  Condenses onto a cooled substrate
Improves control over doping
  Controlled by both temperature and carrier gas flow rate
Better for large-area substrates
http://www.princeton.edu/~benziger/OVPD.pdf

## Slide 15: Inkjet Printing
Process:
  Organic materials diluted into a liquid and sprayed onto substrates, just like a standard inkjet printer
State-of-the-art
Current Research Area
  MIT spinout Kateeva
  Many techniques are proprietary
Organic Vapor Jet Printing
  Developed at Princeton
  Uses vaporized organics instead of the liquid based jets of other inkjet printers
Drastically decreases manufacturing costs and paves the way for flexible and large-screen models
http://www.princeton.edu/~benziger/OVPD.pdf

## Slide 17
Advantages
Relatively easy and cheap to produce
Drastically reduce power consumption of displays
Flexible, foldable, and transparent displays
Disadvantages
Questionable lifespan
  Blue OLEDs currently degrade significantly faster than red and green
Color balance
Water damage susceptibility
Expensive manufacturing
http://www.oled-info.com/files/4DS-transparent-PMOLED-img_assist-351x263.jpg
http://i.ytimg.com/vi/mLMWXBv5rY4/hqdefault.jpg

## Slide 18: Summary
OLEDs are made of organic semiconductors
Discovered by accident by Hideki Shirakawa
Conjugated Bonds and Doping
Physics of Electrophosphorescence
Fabrication
  Vacuum Thermal Deposition
  Organic Vapor Phase Deposition
  Inkjet Printing
Advantages/Disadvantages

## Slide 19: References
http://newsoffice.mit.edu/2015/mass-produced-inkjet-printed-oled-displays-0212
http://www.princeton.edu/~benziger/OVPD.pdf
http://ieeexplore.ieee.org.libpdb.d.umn.edu:2048/stamp/stamp.jsp?tp=&arnumber=1511521
http://electronics.howstuffworks.com/oled7.htm
http://spectrum.ieee.org/tech-talk/semiconductors/materials/organic-glasses
http://spectrum.ieee.org/semiconductors/materials/organic-semiconductor-breakthrough-could-speed-flexible-circuits
http://www.nobelprize.org/nobel_prizes/chemistry/laureates/2000/popular.html

## Slide 20: References(cont.)
http://www.nobelprize.org/nobel_prizes/chemistry/laureates/2000/advanced-chemistryprize2000.pdf
http://www.nature.com/nmat/journal/v11/n10/full/nmat3427.html
http://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=1503740
http://ieeexplore.ieee.org/xpls/icp.jsp?arnumber=973248
http://en.wikipedia.org/wiki/Organic_semiconductor
http://en.wikipedia.org/wiki/OLED

## Slide 21: Questions/Comments?