## Slide 1
Development of a Portable Work Zone
Traffic Safety Information System
using DSRC Based V2I and V2V Communication
M Imran Hayee, Ph. D.
ECE Department, University of Minnesota Duluth

## Slide 2
Outline
What has been accomplished?
  Phase I
  Phase II
What is currently being accomplished?
  Phase III
What could be possible next phase?

## Slide 3
What Has Been Done? – Phase 1
This system was developed and demonstrated in the field
Currently the Bluetooth enabled cell phone gets text messages
MNDOT
Infrastructure
CID
BT enabled
Cell Phone
DSRC-OBU
DSRC
RSU or OBU
Year: 2008 - 2009

## Slide 4
What Has Been Done? – Phase 2
Portable DSRC Based V2I Information System
It was developed and successfully demonstrated in the field.
Can acquire in real time, important travel information e.g., TT and SoC location
Can communicate to the driver, both TT and distance to the SoC location
Uses BT enabled cell phone text messaging as user interface for the driver
Vehicle passing
Through
congested area
Vehicle approaching
Congested area
Work Zone
Start of
Congestion
(varying)
SoC location and TT Broadcast from RSU
End of
Congestion
DSRC-OBU
DSRC-OBU
DSRC-RSU
Distance to SoC
Two way DSRC communication to
acquire safety and traffic data
Year: 2009 - 2010

## Slide 5
System Setup
RSU is placed such that the RSU monitoring range aligns with the end of the congestion.
At periodic intervals, a single OBU participation is requested by the RSU to monitor a vehicle’s speed and position through a congestion area.
RSU sends traffic alert message to OBUs indicating travel time through monitoring area.
RSU
Start of RSU
Monitoring Range
Start of Congestion: Unknown
Work Zone Lane
End of Congestion: Known
End of RSU
Monitoring Range
Desired Location
Coverage range of RSU

## Slide 6
DSRC Communication Protocol
RSU initiates the communication by sending an INVITE message requesting OBU participation.
Each OBU receiving the INVITE message screens itself using the information in INVITE message and if passes the screening, it will respond with the ACCEPT message.
The RSU will screen the incoming ACCEPT messages to ensure that the OBU is on the monitored road, and sends CHOSEN message to the originating OBU of the first ACCEPT message to pass.
OBU periodically communicates NOTIFY messages until EoC point approaching is detected, then RSU is alerted before OBU ceases to send further NOTIFY messages.
OBU
BROADCAST
CHOSEN
INVITE
ACCEPT
NOTIFY
RSU
RSU
OBU

## Slide 7
Detection Problems and Solutions

## Slide 8
Field Testing
The location accuracy of the GPS is the most important factor when determining the possible error in measurements.
The location accuracy error in turn causes errors in distance and direction measurements.
X
(a)
Chart: Location Error (m)
Frequency | 66 | 64 | 37 | 10 | 2 | 1
fgh | 36.67 | 35.56 | 20.56 | 5.56 | 1.11 | 0.56
Culmantive Precentage | 36.67 | 72.22 | 92.78 | 98.33 | 99.44 | 100
(b)

## Slide 9
GPS Distance Accuracy
Urban Area – accuracy is +/- 3 m
Rural Area – accuracy is +/- 2 m

## Slide 10
GPS Direction Accuracy
 | 5 m | 10 m | 15 m
Direction Error | 30 degrees | 14 degrees | 10 degrees
Direction Error decreases if distance is increased
A
A
B
B

## Slide 11
Field Demonstration
The field demonstration site was chosen at Rice Lake Rd, Duluth MN with the focus on providing a clear line of sight between RSU and the OBU.
The RSU is placed near the congestion end due to reduced range on one side due to signal blocking by back of the vehicle.
Start of RSU
Monitoring Range
End of RSU
Monitoring Range
End of Congestion: Known
Start of Congestion: Unknown
N
RSU

## Slide 12
Traffic Safety Parameters
The traffic parameters - Start of Congestion location and the Travel Time are calculated by RSU
The update frequency is determined based upon the TT. If TT is larger, multiple vehicles are chosen at the same time to be monitored.

## Slide 13
Field Demonstration Results
Congestion scenarios of varying start of congestion location and congestion depth were tested for different vehicle speeds.

## Slide 14
What is Being Done? – Phase 3
The Range of the current system is limited to 1 km because of the DSRC antenna range. However the calculated traffic parameters of the system are more useful to the driver if its received earlier. Also congestion or a work zone area may exceed 1 km requiring more range to be covered.
In the current phase 3 (2010-2011), the objective is to utilize the V2V DSRC communication to the developed Portable Work-Zone Safety Message Relay System to
1. Increasing the Message Broadcast Range
2. Increasing the Work-zone Coverage Length

## Slide 15
Increasing the Message Broadcast Range
We intend to increase the message broadcast range using V2V-assisted DSRC communication. To increase the message broadcast range, we propose to use the selected vehicles on the road approaching to work zone to help relay the traffic safety messages backwards to the vehicles following them, to achieve much longer message broadcast range without having an extensive DSRC roadside infrastructure.
1 km
1 km
Portable
DSRC RSU
1 km
V2V
V2V
V2I
V2I

## Slide 16
Increasing the Work-zone Coverage Length
Similarly, we propose to use V2V-assisted communication to cover much longer work zones beyond the access range of one portable roadside DSRC unit. This will be accomplished with the help of selected vehicles present on the work zone well out of reach of the portable roadside DSCR unit to help facilitate V2V-assisted V2I traffic data exchange.
1 km
1 km
Portable
DSRC RSU
1 km
V2V
V2V
V2V
V2I
V2I

## Slide 17
Progress of the Current Phase
Increasing the Message Broadcast Range
1. V2V communication.
2. Develop method for distance measurement adjustment vs. displacement.
3. Develop and test the V2V communication protocol for extended range.
4. Demonstrate the algorithm for distance adjustment in V2V environment
2. Increasing the Work-zone Coverage Length
1. Develop protocols for handling messages from other OBU’s in the OBU program.
2. Develop protocols for extending and contracting the monitored area.
3. Demonstrate the system in field.
Note: The green tasks have been done and the blue tasks are being worked on. The project is expected to finish in time (during June/July 2010 time frame)

## Slide 18
Curve Fitting
The road curvature is statistically modeled by a polynomial fit, parameters of which can be communicated to the OBU so that it can adjust the measured displacement.
Chart: Straight Line Distance (km)
| 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10
 | 0.53 | 1.05 | 1.58 | 2.12 | 2.7 | 3.45 | 4 | 4.55 | 5.2 | 5.85 | 6.98 | 7.62 | 8.15 | 9.08 | 10 | 10.55 | 11.28 | 11.8 | 12.38 | 12.95
 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5 | 4 | 4.5 | 5 | 5.5 | 6 | 6.5 | 7 | 7.5 | 8 | 8.5 | 9 | 9.5 | 10
Start of Congestion
Straight Road
Curved Road
Measured distance

## Slide 19
What Next?
1 km
1 km
Portable
DSRC RSU
1 km
V2V
V2V
V2V
V2I
V2I
Current: V2V assisted V2I
1 km
1 km
1 km
V2V
V2V
V2V
V2I
V2I
Portable
DSRC RSU
Pure V2V ?