## Slide 1: Chapter 5 Simple and Fractional Distillation

## Slide 2: Distillation
Distillation is used to separate two liquids of sufficiently different boiling points.
An equilibrium between vaporizing and condensing in a distillation column allows for the separation of liquids.
Most of the lower boiling liquid is collected in a receiver vial while most of the higher boiling liquid remains in the original flask.
The separation process is improved upon by conducting subsequent re-distillations (simple distillation, Fig. 5.5) or increasing column surface area (fractional distillation, Fig. 5.7).

## Slide 3: Simple Distillation
    1. Add 60 mL of 20% ethanol-water mixture in a 100-mL round-bottomed flask from the macroscale kit.
    2. Add boiling chips.
    3. Assemble apparatus for simple distillation as shown in Fig 5.10 (page 100). Ensure that all the connections are tight. The bulb of the thermometer should be below the opening into the side arm of the distillation head.
    4. Heat the flask strongly on the thermo well (no sand) until boiling begins, then adjust the heat until the distillate drops at a regular rate of one drop per second.
    5. Record both the temperature and volume of distillate at regular intervals. Remember to record the temperature at the first drop of distillate and then after every milliliter that you collect.
    6. After 50 mL of distillate is collected, discontinue distillation and save your distillate for fractional distillation.
    7. Working in the hood, place 3 drops of the distillate using a Pasteur pipette on a Pyrex watch glass and try to ignite it.

## Slide 4: Fractional Distillation
    1. Place the 50 mL of distillate from simple distillation experiment back into the 100-mL round-bottomed flask once it has cooled.
    2. Add boiling chips.
    3. Assemble the apparatus for fractional distillation as shown in Fig. 5.11 (page 102). Use stainless steel wool that will be provided to pack the fractionating column.
    4. Turn up the heat to the electric flask gradually until the mixture just begins to boil. Turn off the power and heat slowly as you watch the ring of condensate rise gradually through the column. This rise should be gradual so that the column can acquire a uniform temperature gradient. Make sure the ring has stopped rising and then increase the heat gradually until distillation starts.
    5. Insulate the column with a towel to prevent flooding of the column as this slows down the distillation.
    6. Record temperature for every milliliter of distillate collected and take more frequent readings as the temperature begins to rise abruptly.
    7. Empty the contents of the graduated cylinder into a 25 mL Erlenmeyer flask once it fills.
    8. Stop the distillation once the second constant temperature is reached.
    9. Repeat the ignition test and note any difference from before.