## Slide 1: Chapter 3 Melting points and Boiling points

## Slide 2: Melting Points
The melting point (mp) of a pure solid organic compound is a characteristic physical property.
Mp’s are dictated by the degree of van-der- Waals, hydrogen bonding, and dipole-dipole interactions between molecules.
Mp determination helps to characterize a compound and indicate purity (mp range).
Determined using a Mel-Temp apparatus and a capillary tube to hold the sample.

## Slide 3: Melting Points
Do calibration of the thermometer using naphthalene (80-82°C) .
Take the melting point of pure urea and cinnamic acid. Take the melting point of pure urea - cinnamic acid mixture. There are three mixtures (1:3, 1:1, 3:1), one group only need to do one.
Determine the melting points of unknowns; all the unknowns are listed on page 54.

## Slide 4: Melting Points (comments)
Tightly pack 2-3 mm of sample into a capillary by tapping a capillary.
If the mp is known, the apparatus can be heated rapidly to within 20°C before slowing the rate of heating to 1°C/minute.
Melting process begins when the first liquid drops are observed and ends when the last trace of solid melts.

## Slide 5: Boiling Points
The boiling point of a pure liquid compound is also a characteristic physical property.
Bp’s are dictated by the degree of van-der- Waals, hydrogen bonding, and dipole-dipole interactions between molecules.
Bp determination does not help to indicate purity, as bp is affected less by impurities.

## Slide 6: Boiling Points
Bp is defined as the temperature at which the vapor pressure of the liquid exactly equals the pressure exerted on it. Therefore, correction for current atmospheric pressure is required.
(P mm Hg / 760 mm Hg) x measured bp = corrected bp

## Slide 7: Boiling Points (comments)
Use the apparatus shown in Figure 3.13 on p. 58.
Thermometer bulb must not touch anything.
Boiling chips are necessary to provide the proper surface for vapor bubble formation.
True boiling is indicated by droplets forming on and dripping from the bulb while observing a constant temperature.
Postlab questions: 5, 6, 7, 13 (pp. 59-60)